###### Robocologie User Manual

# I. Network

###### Illustration 1: Network in OctoPY, at the hardware level
## Central PC:

The central PC is used to communicate with every raspberry pi by using the OctoPY software. Communication is achieved with WiFi by a private network that is managed by the central PC.
As such, is it necessary at first to launch this network so that raspberries pi can connect. This is done by having the central PC connect to the access point. The file /etc/network/interfaces is configured so that the PC can easily be connected to the access point. To connect to the access point, type the following commands:
~$ sudo ifdown eth1 // Not necessary but might be needed when the connection has not	previously been properly cut
~$ sudo ifup eth1 // This may display errors but they are not blocking
~$ ping 192.168.0.100 // This is used to confirm that the PC can communicate with the access	point
~$ ifconfig // It is also safer to validate that the adresse of the PC is correct: 192.168.0.210
When the PC is correctly connected to the access point, it is necessary to start the DHCP server so that raspberries can automatically be issued IP addresses:
~$ sudo /etc/init.d/isc-dhcp-server stop // Again may not be necessary but is more cautious
~$ sudo /etc/init.d/isc-dhcp-server start
Alternatively you can run the script net_conf.sh that runs all commands above. It's located at ./thymioPYPI/OctoPY/net_conf.sh.
~$ bash net_conf.sh
The password will be asked and you will only have to stop the ping command when the router responds.
## Raspberry Pi:

Raspberries are configured so that they can automatically connect to the network at launch. IP addresses are issued between 192.168.0.110 and 192.168.0.150. If an error occurs, it is possible to manually connect to the network by using wicd-curses, which is already installed on the raspberries:
~$ wicd-curses
Here are the network information:
- SSID: NETGEAR_11ng
- Protocol: WPA
- Passphrase: rpiaccesspoint
# II. OctoPY
###### The software used to remotely control the robots is called OctoPY. OctoPY is mainly used to send basic instructions (start, stop etc...) to the raspberries. The software can be found at thymioPYPI/OctoPY/OctoPY.py.
###### You can launch OctoPY as follow :
~$ python OctoPY.py [-h] // The -h argument will show all others arguments available
## Commands:

### Look:
Usage: look [range] [-s save_table]
This command is used to look for the raspberries connected on the network. The default range of IPs on which to look is 192.168.0.111-150 but another range can be given through the range argument. If the argument -s is given, when a raspberry is found, its hostname is retrieved. The association between IP addresses and hostnames is then saved in the hostnames table. This table is saved in a file named hostnames_table.json in the same directory. When OctoPY is started, if this file exists, the hostnames table is loaded so that no look command is necessary if they was no changes in the raspberries connected to the network.

### Send:
Usage: send <message> [hosts_list] [data]
This is the main command that you will use during your experiments. This command is used to send instructions to particular robots (by specifying the hosts_list argument) or every known robot. Additionally, the argument data can be used to send any necessary data with the instruction.
### Messages:
Instructions are sent by specifying a particular message. This message is specified known by its numerical ID, the list of which can also be displayed in OctoPY by taping the TAB key of the keyboard after send has been written. Here is the list of the current messages:
- 0 : INIT: This instruction must always be sent to the raspberries before other instructions can be specified. This is used to launch the main controller on the robots as well as aseba. Any other instruction save OFF will fail on a non-initialized raspberry.
- 1 : START: Launches the experiment specified by the configuration filed loaded on the raspberry. If no configuration file has be previously loaded with the LOAD message then a default experiment will be launched (a simple braitenberg).
- 2 : PAUSE: Pauses a started experiment on the raspberry.
- 3 : RESTAT: Restarts a paused experiment.
- 4 : STOP: Stops the current started experiment.
- 5 : KILL: Stops the controller on the raspberry. For safety, also stop the current started experiment. INIT must be sent again before any other messages can be received by the raspberry (save OFF).
- 6 : OFF: Shutdowns the raspberry.
- 7 : SET: Sets an experiment on the raspberry. The first argument must be configuration file (.cfg file) of the experiment to set then the address(es) of the raspberry(ies).
- 8 : DATA: Used to send any data to a raspberry.
### Hosts list:
The list of raspberries to which the message must be sent can either be precised as an IP address or as a hostname if this hostname exists in the hostnames table (see look command). TAB can be used to display the list of possible hostnames.

### Query:
Usage: query [hosts_list]
Queries the state of the raspberry. This state can be varied:
- Down: The raspberry is off or not connected to the network.
- Sleeping: The raspberry is on and connected to the network but not initialized by the INIT command.
- Listening: The raspberry is initialized.
- Started: An experiment is started on the raspberry.

### State:
Usage: state [hosts_list]
Gives the state (as defined previously) of a list of raspberries according to the a previously executed query command. If no query has already been executed then a query is done.

### Launch:
Usage: launch controller_config_file [-d detached]
Launches a Controller according to its configuration file (.cfg file). When the controller is launched, no other commands can be used.
If the argument -d is given, the controller is detached which means it will run in the background (allowing multiple controllers to run at the same time) while OctoPY can still be interacted with. If -d is not given, a controller can be stopped while executing step() with CTRL+C and will execute postActions() before stopping (please see the controller dedicated section to learn what to do in step and postActions).

### Put:
Usage: put <src_path> <absolute_dest_path> [hosts list]
Use this command if you need to send file(s) from the server to particular raspberries (by specifying the hosts_list argument) or every known raspberries. It uses scp so you can specify similar path arguments.

### Get:
Usage: get <absolute_src_path> <dest_folder> [-r] [hosts list]
Symetric of the previous put command. Use it if you need to get file(s) located at the same place on particular raspberries (by specifying the hosts_list argument) or every known raspberries and send them to the server. Destination on server must be an existing folder so that sub-folders for each host are created inside with an appropriate name. If the argument -r is given, successfully sent files will be removed from hosts.

### Help:
Usage: help <command_name>
At any time in OctoPY, you can use help to display a short help message about the command given in argument.
## Simple Scenario:

This last section is used to illustrate a simple succession of basic instruction in OctoPY, in this case to launch the experiment SimulationBraitenberg.
>> look -s // Gathers the addresses and hostnames of raspberries connected on the network
// If you changed something in the configuration file, send it to every raspberry
>> put rpifiles/experiments/braitenberg.cfg ~/dev/thymioPYPI/OctoPY/rpifiles/experiments
>> send 0 // Initialize all the raspberries
>> set braitenberg.cfg // Loads the experiment on every raspberry, same as “send 7 braitenberg.cfg”
>> send 1 pi2no02 // Starts the experiment on the raspberry pi2no02 only
>> send 1 // Starts every raspberry
>> send 4 // Stops every raspberry
>> send 5 pi2no02 // Kills the controller on raspberry pi2no02
>> send 6 pi2no02 // Shuts the raspberry pi2no02 off

## Monitoring the raspberries:

While it is not necessary to directly connect on the raspberries, it is often useful to check on the execution of the program. First connect to the raspberry by ssh:
~$ ssh pi@<IP address>
The username is thus pi and the password pi also. Then go the folder where the log files are written:
~$ cd ~/dev/thymioPYPI/OctoPY/rpifiles/log
Then you can read the log file as it is written by typing the following command:
~$ tail -F MainController.log
# III. Experiments

Experiments are the programs launched on the raspberries by the OctoPY and constitute the specific behaviours desired for the robots. OctoPY comes with a framework that is intended to facilitate the integration of new experiments. As such, a minimal implementation of an experiment corresponds to coding the behaviour of the robot at each step of the experiment. The code necessary for experiments is in the OctoPY/rpifiles/experiments folder. On the raspberries, the corresponding code can be found at ~/dev/thymioPYPI/OctoPY/rpifiles/experiments. Several experiments already exist to serve as easy demonstrations on how to code an experiment. It is advised to create the experiments on the Central PC and then copy them (with the put command) on every raspberry.
## Creating an experiment:

A script exists to quickly create the files necessary to code an experiment: ./thymioPYPI/OctoPY/rpifiles/CreateExperiment.py.
Usage: python CreateExperiment.py experiment_name
This script creates the basic files and folders that will be used for the experiment experiment_name. More precisely, the following files are created:
./experiments/config_experiment_name.cfg: This file is used to specify the path to the folder and main source file of the experiment which should not be changed. But this file can also be used to specify any parameter that we desire to load with the experiment. Each parameter must be written as follows : type parameter_name = parameter_value
Three different types are recognized when parsing this file: int, float or str. If no type is	given, then str is assumed. Any parameter given in the configuration file may then be	accessed in an experiment by using Params.params.parameter_name.
- ./experiments/experiment_name : This folder contains all the other files created for the experiment. This folder acts as a Python module which is then used by the main controller of the experiments.
- ./experiments/experiment_name/__init__.py: This empty file should often not be changed as it is only used so that the folder is recognized as a Python module.
- ./experiments/experiment_name/readme.txt: This is self explanatory. This file should be used to clearly describe what is the purpose of the experiment.
- ./experiments/experiment_name/SimulationExperiment_name.py: This is the main file where the code will be written. The next section will describe more in the details the content of this file.
## The simulation file:

As previously stated, this file is where the major part of the code will be written (in the first time). When created, its content is at follows:
import Simulation
import Params

class Simulationexperiment_name (Simulation.Simulation) :
def __init__(self, controller, mainLogger) :
Simulation.Simulation.__init__(self, controller, mainLogger)

def preActions(self) :
pass

def postActions(self) :
self.tController.writeMotorsSpeedRequest([0, 0])

def step(self) :
pass

###### In this file is defined the experiment class which extends for the Simulation class defined in the framework. It overrides three functions from its parent class: step, preActions and postActions.
###### step is the most important function to write. When an experiment is started, step is the function called at each step of the experiment. In consequence, this is where most of the code will be called. preActions is used to define all the instructions that must take place when the experiment is started but before the first call of the step function. Finally postActions is used to code the instructions taking place before the experiment is stopped with send 4 or when an error occurs an make the simulation crashes.
## Tools:
To help you coding your experiment, there are some small APIs that already exist and that you can import into your simulation. These APIs are located in ./thymioPYPI/OctoPY/rpifiles/tools.
For now (11/05/2017) there is only one API you can use to facilitate your work with the camera : camera_tools. You may read the README.txt and import it as following in your simulation file :
from tools.camera_tools import <class you need>
## Sending instructions to the Thymio:

Sending instructions to the Thymio is easy as an interface (in the file ThymioController.py) is used to transfer the most basic instructions to the Thymio through aseba. The self.tController property is used to access this controller and interact with the Thymio from your simulation file. These are the instructions that currently exists in the controller:
- readSensorsRequest: Reads the values of the proximity sensors. These values must then be accessed thanks to the getPSValues() function of tController. It returns an array of 7 values in [0, ~ 4300]. 4300 meaning the robot is against a wall.
- readGroundSensorsRequest: Reads the values of the ground sensors. Accessed thanks to the getGroundSensorsValues() function. Return format is a tuple: ([a1, a2], [r1,r2], [d1, d2]). a1 and a2 are in {0, 1} and the others values are in {0, …, 1023}.
- readMotorsSpeedRequest: Reads the speed values of both motors. Accessed thanks to the getMotorSpeed() function. It returns an array of 2 values in [-500, 500] (500 = ~ 20 cm/s).
- readAccRequest: Reads the accelerometer values. Accessed thanks to the getAccValues() function. It returns an array of 3 values in {-32,-31, …, 31, 32} (23 = ~ 1g)
- writeMotorsSpeedRequest: Sends the instruction to move to the robot. The desired speed of each motor is specified as an argument under the form of an array: [left_motor, right_motor]. Each value must be in [-500, 500] (500 = ~ 20 cm/s).
- writeColorRequest: Sends the instruction to change the color of the robot's LED. The desired color is specified as an argument under the form of an array: [R, G, B]. Each value must be in {0,1, …, 32}.
- writeSoundRequest: Sends the instruction to emit a sound. The desired sound is specified as an argument under the form of an array: [frequency in Hz, duration in s].
The Thymio updates its values at a different frequency for each variable. Moreover, your simulation will probably not be synchronized with any of those frequencies, so you may want to know whether your getting a new value or not when calling any getXXXX() function. This may be useful if you need to initialize variable in your preActions() function .
To do so, the function isNewValue(varName) is available and will return true if the value of varName has been updated by the Thymio since the last time you called the getXXXX() function associated to varName, false otherwise. VarName must be a String in {“MotorSpeed", "PSValues", "GroundSensorsValues", "AccValues"}. If used, this function must always be called before the getXXXX() function you'r testing :

“ ” ”
Example 1 : user want to be sure that accelerometer values have been updated since the last time he asked
“ ” ”
self.tController.readAccRequest()
new = self.tController.isNewValue(“AccValues”)
accValues = self.tController.getAccValues()
if new:
# user got new values (Thymio has updated them)
else :
# user got previous values (Thymio has not updated them yet)
“ ” ”
Example 2 : user wants to initialize accelerometer values in preAction()
“ ” ”
new = False
while not new:
self.tController.readAccRequest()
new = self.tController.isNewValue(“AccValues”)
time.sleep(0.1) # avoid flooding thymio since its frequency is ~ 10Hz
accValues = self.tController.getAccValues()

The document https://aseba.wdfiles.com/local--files/fr:asebausermanual/ThymioCheatSheet_fr.pdf shows everything you need to know about the Thymio and even more.
## Communicating with other robots:

Robots can communicate with each other by using the sendMessage from the parent Simulation class.
Usage: self.sendMessage(recipients = recipientsList, value = value)
The recipientsList corresponds either to a list of IP addresses or hostnames as when using OctoPY.
To receive a message, the function receiveComMessage must be overrided.
Usage: def receiveComMessage(self, data)
data[“senderHostname”] contains the sender hostame data[“value”] contains the message's value.
# IV. Controllers

Controllers are used to automate the instructions that are sent by OctoPY so that it not necessary to manually type them. As for experiments, controllers can be created with a script called CreateController.py (./OctoPY/CreateController.py). All controllers are located in ./thymioPYPI/OctoPY/controllers. And again as for experiments, this script will create a configuration file (.cfg file) and folder containing a file with basic code for a controller :
import Controller
import Params

class ControllerName(Controller.Controller) :
def __init__(self, controller, mainLogger) :
Controller.Controller.__init__(self, controller, mainLogger)

def preActions(self) :
pass

def postActions(self) :
pass

def step(self) :
pass

def notify(self, **params) :
pass

Similarly to experiments, there are three main functions to override: preActions, step, and postActions. By using the property self.OctoPYInstance, it is possible to use OctoPY commands in the same way as with the interactive version. Typically, preActions will be used to initialize and start experiments, postActions to stop the experiments and shut the raspberries down and step to code the behaviour of the controller while experiments are running.
The most useful behaviour of a controller while experiments are running is to listen to the raspberries. This can be done by registering the controller to particular raspberries. This is done with the function register. Then, overriding the function notify allows to code the behaviour of the controller when notifications are received from the raspberries listened to. You can check the controller TestNotifications to have an example on how to code such a controller.
# V. Setting a Raspberry

Most of the raspberries are already configured. But it may be necessary to set new rasperries when the time comes. Fortunately, this is easy.

The first step is to write the default system image on the SD card. The newest images is present on the computer at: ~/rpiImage_pi3noXX_2016_12_15.img
To write this image on the SD card, first find the devices mounted on the computer:
~$ df -h
Then, find the partition on which the SD card is mounted. It should be listed as something as /dev/sdc1 and /dev/sdc2. You can unmount the device by typing the following command:
~$ umount /dev/sdc1 // If /dev/sdc1 is the partition on which the SD is mounted

You can then copy the system image on the SD by using the following command:
~$ dcfldd bs=4M if=<system_image> of=<partition>
This should take some time. If you need more information, please read https://www.raspberrypi.org/documentation/installation/installing-images/linux.md

As this image is copied to every raspberry, there are some changes that necessary to do so that each raspberry can be unique. First it is necessary to change the hostname of the raspberry. Each raspberry hostname should read as follows: pi<raspberry_version>no<raspberry_number>. For example, for the third raspberry pi 2, its hostname is pi2no03. Whatever the raspberry's version (2 or 3), please keep the raspberry numbers successive. To change the hostname of a raspberry, first modify the file /etc/hosts. Find the line that reads:
127.0.1.1	raspberrypi
and change raspberrypi by the new hostname. Then open the file /etc/hostname and replace the hostname by this new hostname.
You also need to change the machine-id so that each agent as an unique one. To do that, type the following command:
~$ dbus-uuidgen > /var/lib/dbus/machine-id

The system image may not have the last version of the code available on the git repository. As such, you need to pull the last version of the code from the git. There is a basic git account created to pull (and not push) code from the git. Its credentials are:
- Username: ThymioPYPI
- Password: xxxxx (please ask Nicolas Bredeche)
Then, to pull the code move into the ~/dev/thymioPYPI directory and type the following command:
$~ git pull origin master

# VI. Files Location

This section is used to summarize the location of the different files and folders on the thymioPYPI repository:
- thymioPYPI/OctoPY contains all the files used by the OctoPY framework
  - ./controllers: contains the controllers and their configurations files
  - ./log: contains a log of all commands typed in OctoPY when launched with the -L argument
  - ./rpifiles: folder containing all the files that are supposed to be used on the raspberries
    - ./experiments: contains the experiments and their configurations files
    - ./filesNetworking: folder containing a copy of all the files that are used to configure the network.
    - ./log: contains the log of the part of OctoPY that runs on the raspberry as well as the experiments log.
    - ./standAlone: projects or pieces of code that run independently of OctoPY (they are not experiments so you need to manually launch them from a ssh connexion)
    - ./tools: contains small APIs that can be used in your experiments
- Every other folder contains project from students who have worked with the Thymios (but not necessarily using OctoPY)
  - thymioPYPI/p_androide-SOTO_SHAMS: M1 ANDROIDE project. They upgraded OctoPY and used it to implement Embodied and Distributed evolutionary algortihms (experiments FollowLightGen and FollowLightGenOnline)
  - thymioPYPI/robocologieimage: source code for the tracking and monitoring software.
  - thymioPYPI/RFID: simple test code to use the bar scanners.
  - thymioPYPI/TagRecognition: source code and data for tag recognition. Most of the useful code is also present in thymioPYPI/OctoPY/rpifiles/standAlone/TagRecognition.
# VII. Manual History

This section keeps history of every modification of the manual.
- 05/02/2017 : 'put' and 'get' commands added at the end of the section Commands of II. OctoPY. Paragraph of introduction in III. Experiment changed accordingly.
- 06/02/2017 : instructions to run the net_conf.sh script added in the section Central PC of I. Network.
- 20/03/2017 : instructions to get accelerometer values added in the section Sending instructions to the Thymio of III. Experiments.
- 07/05/2017 : instructions to stop a controller added in II. OctoPY → Commands → Launch
- 09/05/2017 : instructions send 5 updated in II. OctoPY → Commands → send + examples added in Sendings instruction to the Thymio in III. Experiments
- 11/05/2017 : VI. Files locations updated, VIII. Appendices added, III. Experiments → Tools added
# VIII. Appendices

## Appendice 1: OctoPY diagram

###### Illustration 2: Full diagram of the OctoPY framework
## Appendice 2: In case of emergency

If your having big troubles when trying to start a simulation and you already tried to send 5 and send 0 again you can either reboot the raspberry or try the following sequence :
~$ ssh pi@<IP address> // connect to the raspberry that causes the problems
~ $ ps aux
// In the list, look for the PIDs of process whose owner is PI and corresponding to :
// – MainController.py
// – Asebamedulla
// – Any ssh connection that is not the one you are using right know
~ $ kill <list of PIDs you just determined>